The A09 Switch

Wiring as follows-
L Black – Power
1 Common from capacitor
2 Larger reading from capacitor
3 Smaller reading from capcitor

Capacitor should have at least 3 wires of different colors or could have 4 or 5 wires with 2 or 3 uf readings.

Some switch brands such as KTE and Santa will have the power in the 2 position on the switch. In this case you will move the wires when connecting the new A09 switch as follows-
Old	New
Cap Common L	Black Power
Larger Cap 1 Cap Common
Black Power 2 Larger Cap
Smaller Cap 3 Smaller Cap